## Using the library in IO board
190421, updated 30.5.2019/pekka
An IO board communication is typical use for the IOCOM library. I usually power IO boards by ARM32 micro controller. Resources are limited and reliability is the key requirement. Typical choices are:
- We do prefer single threaded model over multi threaded. A programming which crashes the micro controller, locks up the network or shifts timing is far more likely to pass through testing unnoticed in multi threaded programming than in single threaded.
- We stay away from heap based memory allocation, since memory leak or fragmentation could cause reliability problems over long run. Rather memory is allocated globally, from stack or from application managed memory pool.
### API for an IO board
The ioc_ioboard.c collects IOCOM functionality needed by an IO board into simple to use API calls.
### Single thread - IO board software organization
If IO board code runs on bare metal, it is single thread mode: typical initialization and main loop organization is used. Main loop must never pause. The IOCOM can also be used in multi threaded with RTOS, etc. See ? for information.
### Mapping the memory blocks to inputs and outputs
Unless there is significan benefit in bit packing, it is easiest to use 1 digital input or output = 1 byte in memory block. Support for bit packing digital inputs and outputs adds some complexity. In most cases, there is too small performance benefit compared to added complexity.
### State machines
In single thread mode we can never call sleep() etc. State machines are simple way to generate code which will execute a timed sequence or loop without pausing the IO board’s main loop.