## Low level access to memory block content
190622, updated 23.6.2019/pekka
Memory block content is the actual data to be transferred. It is accessed using functions, which change the content and cause changes to be propagated.
### Writing data to be transferred
The ioc_write is the generic function to set data to be transferred.

void ioc_write(
    iocMemoryBlock *mblk,
    int addr,
    os_uchar *buf,
    int n);

There are simple funtions to set one typed value. These set 8 bit integer value (1 bytes), 16 bit integer value (2 bytes), 32 bit integer value (4 bytes), 64 bit integer value (4 bytes) and 32 bit floating point value (4 bytes). These functions take care that values are stored least significant byte first order within memory block, regardless of processor architecture. These functions convert longer (or same length) integer type, so we do not need to care wether value is signed or unsigned.

void ioc_set8(
    iocMemoryBlock *mblk,
    int addr,
    os_int value);

void ioc_set16(
    iocMemoryBlock *mblk,
    int addr,
    os_int value);

void ioc_set32(
    iocMemoryBlock *mblk,
    int addr,
    os_int value);

void ioc_set64(
    iocMemoryBlock *mblk,
    int addr,
    os_int64 value);

void ioc_setfloat(
    iocMemoryBlock *mblk,
    int addr,
    os_float value);

### Writing string
String is written by ioc_write() function:

void ioc_setstring(
    iocMemoryBlock *mblk,
    int addr,
    const os_char *str,
    int n);

For example:

ioc_clear(mblk, addr, “teststrings”, 10);

The example above writes always 10 bytes to wipe out any previous value. Resulting string in memory block has maximum nine characters followed by at least one ‘\0’ character. Strings should be UTF-8 encoded and always terminated with ‘\0’ character.

### Writing arrays
Writing arrays element at a time is somewhat waste or processor time and if IOC_AUTO_SEND flag is set, generates extra data transfers. Use functions to write typed arrays into memory block:

void ioc_setarray16(
    iocMemoryBlock *mblk,
    int addr,
    os_short *arr,
    int n);

void ioc_setarray32(
    iocMemoryBlock *mblk,
    int addr,
    os_int *array,
    int n);

void ioc_setfloatarray(
    iocMemoryBlock *mblk,
    int addr,
    os_float *array,
    int n);

Here n is number of array elements, not number of bytes. You may notice that array functions for bytes and for 64 bit integers are missing. For simple byte data this is because the function would be the same as ioc_write(). Reason for missing 64 bit array function is that I cannot imagine where it would be needed (can be added if someone really needs it).
### Clearing range in memory block
The ioc_clear() function sets range of bytes starting from address given as argument to zero. This is preferred way to clear memory block data.

void ioc_clear(
    iocMemoryBlock *mblk,
    int addr,
    int n);
### Propagating writes to transfers
Propagating changes is done by ioc_send() function. This function is called automatically if IOC_AUTO_SEND flag was given when the memory block was initialized. Similarly received data is propagated by ioc_receive() function, and flag to call it automatically is IOC_AUTO_RECEIVE.
### Reading received data
Similarly to writing to outgoing memory block, we can read incoming memory block. Data can also be read from outgoing memory block, but never write to incoming memory block. Generic read function is as:

void ioc_read(
    iocMemoryBlock *mblk,
    int addr,
    os_uchar *buf,
    int n);

The read functions for simple values are:

os_int ioc_get8(
    iocMemoryBlock *mblk,
    int addr);

os_int ioc_get8u(
    iocMemoryBlock *mblk,
    int addr);

os_int ioc_get16(
    iocMemoryBlock *mblk,
    int addr);

os_int ioc_get16u(
    iocMemoryBlock *mblk,
    int addr);

os_int ioc_get32(
    iocMemoryBlock * mblk,
    int addr);

os_int64 ioc_get64(
    iocMemoryBlock *mblk,
    int addr)

os_float ioc_getfloat(
    iocMemoryBlock *mblk,
    int addr);

void ioc_getstring(
    iocMemoryBlock *mblk,
    int addr,
    const os_char *str,
    int n);

When reading, we may convert to longer integer type, thus sign conversion matters. Thus there are unsigned version of ioc_get8u, ioc_get16u and ioc_get32u. 64 bit integers are assument to be always signed.

### Reading arrays
Same as for writing, data can be read as arrays. Here n is number of elements, not number of bytes.

void ioc_getarray16(
    iocMemoryBlock *mblk,
    int addr,
    const os_short *arr,
    int n);

void ioc_getarray32(
    iocMemoryBlock *mblk,
    int addr,
    const os_int *array,
    int n);

void ioc_getfloatarray(
    iocMemoryBlock *mblk,
    int addr,
    const os_float *array,
    int n);

### Detecting received data using callback function
Using callback function to react to received data is usually much more efficient than polling for changes. Application implemened callback function could be something like:

static void iocontroller_callback(
    struct iocMemoryBlock *mblk,
    int start_addr,
    int end_addr,
    os_ushort flags,
    void *context)
{
    /* Echo 2 bytes at address 2 back to IO board address 11. This happens
        practically immediately.
     */
    if (end_addr >= 2 && start_addr < 2 + 2)
    {
        os_int command_echo = ioc_get16(mblk, 2);
        ioc_set16(c->outputs, 11, command_echo);
    }
}

Use ioc_add_callback to set the callback function:

ioc_add_callback(mblk, iocontroller_callback, OS_NULL);

There are few things to be aware of when using callbacks:
- Callback must return almost immediately, it cannot have long processing and even debug prints slow down communication significantly. If callback needs to initiate loger process, trigger an event or set a flag from the callback function.
- In multithread operation, the callback function can is called by other thread than which runs the sequence. Typically thread running the communication.

### About thread safety
If multithreading support is enabled for eosal and iocom when compiling, memory block access is thread safe. These functions can be called from multiple threads.