## Data compression
180728, updated 18.5.2019/pekka
Over lossless connection we have to pass only initial state and later on just changes. To compress the only changes we keep record of previous data sent in transfer buffer.

delta[i] = data[i] – prev_data[i]

This is done just with 8 bit integers, overflow ignored. Typically most of diff[i] values are zeroes, since in most cases much of data does not change. So we use zero-run compression:

1. Repeat while we have data left. Interrupt with -1 if compressed data is as long or longer than original data.
2. Count how many nonzero bytes there are starting from current byte p. Count up to maximum 255 bytes. Do not interrupt count to one stand alone zero
3. Write number of nonzero bytes.
4. Write nonzero bytes.
5. Calculate number of zero by
6. Count how many zero bytes there are starting from current byte p. Count up to maximum 255 bytes.
7. Write number of zero bytes.
8. Go back to step two.

p = pointer to data to compress.
bytes = number of bytes to compress.
dst = destination buffer for compressed data.
dst_sz = destination buffer size in byte.
returns number of bytes in destination buffer or -1 if is not compressed (longer than original).

int ioc_compress(
    os_uchar *srcbuf,
    int *start_addr,
    int end_addr,
    os_uchar *dst,
    int dst_sz)
{
    os_uchar
        *dst_start,
        *dst_end,
        *p,
        *start;
    int
        bytes,
        count,
        dst_count,
        max_count;
    dst_start = dst;
    dst_end = dst + dst_sz;
    p = &srcbuf[*start_addr];
    bytes = end_addr - *start_addr + 1;
    while (bytes > 0)
    {
        start = p;
        count = 0;
        max_count = bytes;
        if (max_count > 255) max_count = 255;
        while ((p[0] || p[count < max_count-1 ? 1 : 0]) && count < max_count)
        {
        count++;
        p++;
        }
        bytes -= count;
        if (dst + count >= dst_end)
        {
        p = start;
        break;
        }
        *(dst++) = count;
        while (count--) *(dst++) = *(start++);
        if (bytes == 0) break;
        start = p;
        count = 0;
        max_count = bytes;
        if (max_count > 255) max_count = 255;
        while (*p== 0 && count < max_count)
        {
        count++;
        p++;
        }
        bytes -= count;
        if (dst >= dst_end)
        {
        p = start;
        break;
        }
        *(dst++) = count;
    }
    count = p - &srcbuf[*start_addr];
    *start_addr = p - srcbuf;
    dst_count = dst - dst_start;
    return dst_count < count ? dst_count : -1;
}

The outgoing message will contain “delta encoding” and “zero run compression” bits in header. If compression result would be as long or longer than data in uncompressed format, compression is not done. The delta encoding is not done at least for the first snapshot to send. Data received should use these bits to detect if data is delta encoded or compressed to read it.

## Uncompress data
This is simpler to implement than compression:

1. Start from first source byte to process.
2. Quit if we have processed all source data.
3. Get next source byte in n. It is count of real data bytes.
4. Move n data bytes from source to destination.
5. Quit if we have processed all source data.
6. Get next source byte in n. It is count of zero bytes.
7. Write n zero bytes to destination
8. Back to step 2.
In addition we must check that we do not overflow destination buffer, in case our source data is erroneous. Undoing delta encoding is also simple. We add received delta values to previous values.

data[i] = data[i] + delta[i]

This is again done just with 8 bit integers, overflow ignored.