## Data transfer framing
180728, updated 22.6.2019/pekka

Serial frame.
name/address	bytes	type	use
FRAME_NR/0	1	uchar	Frame count. Every time new frame is sent, this number is incremented, value 0 if used to indicate the first frame and skipped from that point on. Used to check for missing or duplicated frames, first frame, etc. Value 255 is used as ACKNOWLEDGE/KEEP ALIVE. Also values greater than 220 are reserved for control characters.
CHECKSUM/1	2	ushort	Checksum. 16 bit CRC. Used to verify frame integrity.
FLAGS/3	1	uchar	Flags: IOC_DELTA_ENCODED, IOC_COMPRESESSED, / IOC_ADDR_HAS_TWO_BYTES, IOC_ADDR_HAS_FOUR_BYTES, IOC_MBLK_HAS_TWO_BYTES, IOC_SYNC_COMPLETE
BYTES/4	1	uchar	Data size, bytes. Compressed or uncompressed. Data size zero indicates special message. In this case start address is parameter for special message.
MBLK/5	1/2	uchar/ushort	Memory block identifier.
ADDR/6-7	1/2/4	uchar/ushort/uint	Start address within memory block. Or for special messages like keep alive or request to bind, this is 32 bit value containing both special message and argument for it.
DATA/7-11	?	uchar[]	Data. Can be delta encoded and/or compressed.

Socket frame.
name/address	bytes	type	use
FLAGS/0	1	uchar	Flags: IOC_DELTA_ENCODED, IOC_COMPRESESSED, / IOC_ADDR_HAS_TWO_BYTES, IOC_ADDR_HAS_FOUR_BYTES, IOC_MBLK_HAS_TWO_BYTES, IOC_SYNC_COMPLETE / Value 255 reserved for ACKNOWLEDGE/KEEP ALIVE.
BYTES/1	2	ushort	Data size, compressed or uncompressed, bytes. / Data size zero indicates special message. In this case start address is parameter for special message.
MBLK/3	1/2	uchar/ushort	Memory block identifier.
ADDR/4-5	1/2/4	uchar/ushort/uint	Start address within memory block. Or for special messages like keep alive or request to bind, this is 32 bit value containing both special message and argument for it.
DATA/5-9	?	uchar[]	Data. Can be delta encoded and/or compressed.

All numeric data is transferred in small endian form, lest significant byte first and most significant byte last.

Maximum frame sizes for different types of communication are fixed. For all serial communication maximum message frame size is always 96 bytes (IOC_SERIAL_FRAME_SZ), which includes headers. For sockets maximum message frame size is set 464 bytes (IOC_SOCKET_FRAME_SZ). Maximum frame sizes (especially for serial communication) are small to work with limited memory in micro-controllers. Notice that multiple message frames can be packed in single TCP frame.